Adaptive PID tuning using Recurrent Neural Networks

Robot description:
The robot is an autonomous cart, used in industries and warehouses. The navigation is done using navigation stack in ROS, with a low level PID controller using Arduino Mega 2560 for motors and IMU, XBOX kinect and odometry data as inputs.

Problem analysis:
1. The low level pid controller parameters needs to be changed with respect to time according to the variation in the eternal factors like friction, battery level, slipping of wheels, etc..
2. Also, there is an angle drift in the movement of the bot during a straight line motion.
3. A considerable delay is recorded in the step response of the motors due to which the time response parameters (time constant, settling time..) are greater than the expected.

Proposed Solution :

- A PID auto tuning structure combined with system identication is proposed, in order to cater to the varying nature of the system.
- It consists of two neural networks [1], one for system identification(offline) and the other for auto PID tuning(online).
- Once the plant model has been identified, it is used as the system for real time tuning of the PID values.

Plant identification neural network :

The system is given a constant PWM input to identify the step response of the system
A range of inputs are stored in an array with each having a delay of 50 milliseconds ( Update interval ).
The output is calculated using Auto regressive moving average model [2]
Input nodes :
PWM value (step input), velocity value from the odometry data
Output nodes:
Gain (k) and time constant (tau) – considering the system to be first order
Hidden nodes: a and b layers (each with 6 nodes)
Activation function: hyperbolic tangent inverse function

Neural network for auto tuning:

Using neural network, estimate the Kp, Ki parameters real time
Using the model obtained from plant identification neural network, second order system is obtained and velocity is calculated [3].
Input nodes: rise time (tr), settling time (ts), peak overshoot (eos)
Output nodes: Kp, Ki

Problems to be solved:
Change in system behaviour with respect to PWM should be addressed.

Possible solution:
ANN can be used instead of RNN for plant identification so that a unified K and time constant for all PWM values is obtained. But due to computational inefficiency of Arduino, it should be implemented using a single board computer.

Documentation:

ml_trial7_final.ino – plant identification neural network
outer_nn_dummy.ino – new version of auto tuning
outer_nn.ino – old version of auto tuning
pwm_vel_orig.ino – without PID velocity output
ArduinoANN.ino – artificial neural network example
result_finale.ods - output results for plant identification and tuning

References:
[1] Recurrent Neural Networks for PID Auto-tuning Adaptive Control and Identification of Nonlinear Systems Elias Reichensdörfer, Johannes Günther, Klaus Diepold
[2] Approximating Transfer Functions using Neural Network Weights Tarek A. Tutunji Mechatronics Engineering Department Philadelphia University Amman, Jordan
[3] Towards Explicit PID Control Tuning using Machine Learning Andrew Zulu, member, IEEE Department of Mechanical and Marine Engineering Namibia University of Science and Technology Windhoek, Namibia